## Slide 1: B2X 2차년도 3차 Pilot Study
Analysis of EEG data from the taVNS experiments
- N=20

## Slide 2
Experiment Protocol
BIOPAC 세팅 | 
Sampling rate | 1000 Hz
ECG | Lead Ⅰ
PPG | 오른손 검지
GSR | 오른손 중지, 약지
VOD | 눈이 보이도록
Subject | 
Posture | Lying down
Eyes | Open
눈 ~ 태블릿 거리 | 50-100 cm
Fixed parameters | 
Electrode location | Left cymba concha
Pulse width | 200 us
Frequency | 
20 Hz | 100 Hz
1 | 2
S020 | S100
N020 | N100
Waveform | Biphasic symmetric | A
 | Biphasic | B

## Slide 3: EEG Setting
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Empty | Fc5 | F7 | C3 | P3 | P7 | Cp5 | T7
9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
F4 | Fc6 | F8 | C4 | P4 | P8 | Cp6 | T8
17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Pz | Poz | O1 | Oz | O2 | Fc1 | Fc2 | Cz
25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Cp1 | Cp2 | Fp1 | Fpz | Fp2 | Fz | A1 | F3
EEG 세팅 | 
Sampling rate | 512 Hz
Gain | 239
REF
GND
33 | Reference | Gnd
flag | A2 | Afz
0
Time

## Slide 4: Framework of Analysis
Data Extraction
- Acquire 34ch cdf files (ch1: time, ch2: noise, ch34: flag)
cdf  txt: manually using telescan
txt  mat: python programming (ch1, ch2, ch34 are removed)
Result: .mat files that contain 31ch EEG data
2. .locs file preparation
Based on 10-20 system
32 ch
3. mat2set
Convert mat file to set file